## Slide 1
MASTER THESIS PROJECT
Presented by 2022AIM1007
Supervised by - Prof. Jagpreet Singh

## Slide 2
CONTENT
01
02
03
04
05
06
07
INTRODUCTION
PROBLEM
LITERATURE REVIEW
RESEARCH OBJECTIVES
METHODOLOGY
RESULTS
UPCOMING WORK

## Slide 3
Over the past decade, Wireless Sensor Networks (WSNs) have gained increasing traction for real-world data collection. WSNs typically consist of battery-powered sensor nodes, but limited battery capacity hinders their operational lifespan. To address this, various approaches have been proposed, including energy conservation and battery replacement.
A breakthrough in Wireless Power Transfer (WPT), particularly magnetic resonant coupling , offers an alternative solution to recharge sensor node batteries. WPT provides advantages like resilience to environmental conditions, precise power control, and conductor-free charging .
Wireless charging has gained significant attention as a means to extend sensor node lifespans. This research focuses on optimizing system performance through strategic wireless charger deployment.
INTRO
DUCTION
page 2

## Slide 4
In our research, our work revolves around the problem of minimizing charger placement while ensuring that the energy needs of each sensor node are adequately met. This entails devising a strategic approach for positioning wireless chargers from a random set of candidate locations. The primary objectives are to fulfill the energy requirements of individual sensor nodes while simultaneously minimizing the overall number of utilized chargers.
Moreover, we establish the NP-hardness of the problem . For directional charging scenarios, we use different methodologies of placement and then select the best one with comparison. In the case of directional charging, we initiate the process by extracting candidate orientation sets for each candidate charger location. This reduces the search space from an infinite range to a finite set. Subsequently, we hope to propose a algorithm with a proven performance guarantee.
Finally, our research findings would be substantiated through extensive numerical simulations, where we employ directional antennas and employ the vertex cover algorithm to optimize charger placement.
page 3

## Slide 5
j
  Energy Limitations: Sensor nodes in WSNs rely on limited onboard battery capacity.
  Network Longevity: The constrained energy capacity of sensor nodes restricts the operational lifespan of WSNs.
  Charger Placement Complexity: Traditional charger placement strategies may not maximize network efficiency.
PROBLEM
page 4
WIRELESS CHARGER PLACEMENT
OPTIMIZATION IN WSN

## Slide 6
Literary Review
Page 06
"Optimal Wireless Charger Placement with Individual Energy Requirement"
  Authors: Xingjian Ding, Jianxiong Guo, Deying Li, Weili Wu
  Focus: Optimal charger placement in WSNs with individualized energy requirements.
  Contribution: Proposes a novel methodology for strategic charger placement based on sensor node energy needs.
  Result: Enhanced network lifetime and improved energy efficiency
Literary Review
01
Literary Review
02
"Wireless Power Transfer and Energy Harvesting in Distributed Sensor Networks: Survey, Opportunities, and Challenges"
  Authors: Gerald K Ijemaru, Kenneth Li-Minn Ang, Jasmine KP Seng
  Focus: Comprehensive survey of WPT and energy harvesting in sensor networks.
  Insights: Reviews various techniques and technologies, highlighting opportunities and challenges.
  Significance: Provides a holistic overview of the field, guiding future research directions

## Slide 8
Develop an Optimized Charger Placement Strategy
  Create a novel methodology for strategically placing wireless chargers in WSNs in directional domain.
  Tailor charger placement to minimize number of antennas , maximizing energy utilization.
OBJECTIVES
page 6
Objectives 1
Quantify the Impact on WSN Performance
  Conduct comprehensive simulations to assess the effectiveness of the proposed charger placement strategy.
  Provide clear quantitative evidence of the benefits achieved by the optimized charger placement approach.
Objectives 2

## Slide 9
METHO
DOLOGY
page 7
Step 1: Charger Placement Simulation
  Charger placement at every node .
  Consider various charger locations and angles to ensure adequate coverage.
Step 2: Node Coverage Assessment
  For each charger location and angle, assess the coverage range of wireless charging.
  Identify the sensor nodes within the coverage area of each charger
Methodology 1- BASELINE
Step 1: Randomly select charger locations within the WSN deployment area.
  Randomly assign charging angles for each charger, considering a range of orientations.
Step 2: Node Coverage Assessment
  Assess the coverage range of each randomly placed charger with its angle and Identify the sensor nodes located within the charging coverage area of each charger
Methodology2 -Random Placement

## Slide 10
Selection of Platforms to work on e.g. MATLAB,OMNET ,SI MULINK etc.
01
PLATFORM
02
03
04
GUI based or code based simulation of the network and wpt placement to generate results
SIMULATION
Generation of Data for various paramters e,g. Area, Density, Nodes, Angle etc.
DATA GEN
Removing noise from the output data and collecting unbiased useful data to be used as perfomance metric in comparing methodologies
DATASET
IMPLEMENTATION

## Slide 11
Results
Page 9

## Slide 12
Results
Page 10

## Slide 13
Results include simulation of wsn and provides data of sets with omnidirectional Antenaa placement to be known or entered by the user
It generates dataset of nodes which recieved power sufficient to operate.
.
Furthermore building up on methodologies using Dataset provided by the Supervisor.
Work on Baseline methodology has been in progress as directional component has to be included yet.
DISCUSSION
11

## Slide 14
QUESTIONS

## Slide 15
REFERENCES
F.K. Shaikh, S. Zeadally, Energy harvesting in wireless sensor networks: a comprehensive review, Renew. Sustain. Energy Rev. 55 (2016) 1041–1054
H. Dai, X. Wang, A.X. Liu, H. Ma, G. Chen, Optimizing wireless charger placement for directional charging, in: IEEE INFOCOM 2017-IEEE Conference on
Computer Communications, IEEE, 2017, pp. 1–9
Wireless power transfer and energy harvesting in distributed sensor networks: Survey, opportunities, and challenges
Gerald K Ijemaru, Kenneth Li-Minn Ang https://orcid.org/0000-0002-2402-7529 lang@usc.edu.au, and Jasmine KP Seng

## Slide 16
THANK YOU